Detecting Finite Bandwidth Periodic Signals in Stationary Noise using the Signal Coherence Spectrum

Melvin J. Hinich

Applied Research Laboratories

University of Texas at Austin

P. O. Box 8029

Austin, Texas 78713-8029

Phone: +1 512 471 5121

Fax: +1 512 835 3259

hinich@mail.la.utexas.edu

Phillip Wild

Centre for Economic Policy Modeling, School of Economics,

University of Queensland,

St Lucia, QLD, 4072, Australia

Phone:+61 7 3346  9258

Fax: +61 7 3365 7299

p.wild@economics.uq.edu.au

##### Abstract

All signals that appear to be periodic have some sort of variability from period to period regardless of how stable they appear to be in a data plot. A true sinusoidal time series is a deterministic function of time that never changes and thus has zero bandwidth around the sinusoid’s frequency. A zero bandwidth is impossible in nature since all signals have some intrinsic variability over time. Deterministic sinusoids are used to model cycles as a mathematical convenience. Hinich (2000) introduced a parametric statistical model, called the Randomly Modulated Periodicity (RMP) that allows one to capture the intrinsic variability of a cycle. As with a deterministic periodic signal the RMP can have a number of harmonics. The likelihood ratio test for this model when the amplitudes and phases are known is given in Hinich (Hinich, 2003). A method for detecting a RMP whose amplitudes and phases are unknown random process plus a stationary noise process is addressed in this paper. The only assumption on the additive noise is that it has finite dependence and finite moments. Using simulations based on a simple RMP model we show a case where the new method can detect the signal when the signal is not detectable in a standard waterfall spectrogram display.

Keywords: Randomly modulated signal, signal coherence spectrum, periodic, periodogram, spectrogram, waterfall display

Introduction

Consider the classic problem of detecting a sinusoid in additive noise. Suppose that the discrete-time sampled signal is of the form  where  denotes the noise at time  where  is the sampling interval. Assume that the amplitude  and phase  of the sinusoid are unknown parameters. If the frequency  is known and the null hypothesis is that  then the standard test of this hypothesis is to use the Fisher periodogram test (Fisher, 1929). The periodogram of a block of the signal is  where  is the kth Fourier frequency and . In contrast for most signal processing applications, such as sonar and radio astronomy, a large peak at frequency  in the periodogram is assumed to be generated by a sinusoid in the signal at that frequency if there is a credible reason for the existence of a sinusoid at that frequency. In other words the usual signal processing practice of detecting sinusoids is not treated as a formal statistical problem.

All signals that appear to be periodic have some sort of variability from period to period regardless of how stable they appear to be in a data plot. A true sinusoidal time series is a deterministic function of time that never changes and thus has zero bandwidth around the sinusoid’s frequency. A zero bandwidth is impossible in nature since all signals have some intrinsic variability over time.

In active sonar the outgoing acoustic pings are virtually the same from ping to ping. But each received sonar ping has some random modulation. The amount of ping to ping variation in the receive signal is surprisingly large. A passive sonar signal has a lot of modulation due to the scattering and reflections in the water.

Deterministic sinusoids are used to model cycles as a mathematical convenience. It is time to break away from this simplification in order to model the various periodic signals that are observed in fields ranging from biology, communications, acoustics, astronomy, and the various sciences.

Hinich (2000) introduced a parametric statistical model, called the Randomly Modulated Periodicity (RMP) that allows one to capture the intrinsic variability of a cycle. As with a deterministic periodic signal the RMP can have a number of harmonics. The likelihood ratio test for this model when the amplitudes and phases are known is given in Hinich (Hinich, 2003). In that paper, the detection problem was structured around a simple null (gaussian white noise) and a simple alternative (a known sinusoid plus gaussian noise). The main result was that the optimal detector for this problem was a linear combination of the periodogram and a matched filter. The Fisher periodogram test was demonstrated to be sub optimal if there was prior knowledge of the modulation.

In this paper we significantly extend this work by addressing the more   realistic (and complicated) detection problem for a RMP whose amplitudes and phases are, themselves, complicated random processes .In contrast to the detection problem presented in Hinich (2003), the alternative process in this paper is much more general. In fact this generalization is achieved by not actually requiring any specification of the nature of the modulations apart from requiring a joint density and finite dependence.

A randomly modulated periodicity

A discrete-time random process  is an RMP with period  and K harmonic frequencies  if it is of the form

where the  and  are constants. The modulation processes  are unknown random processes with zero means, finite cumulants and a joint distribution that has the following finite dependence property: and  are independent if  for some D and all  and all sample times. The modulations increase the bandwidth of the signal above the highest harmonic. Therefore the sampling frequency  must be greater than twice the highest frequency of the signal in order to avoid aliasing.

Finite dependence is a strong mixing condition Billingsley (1979). If  then the modulations are approximately stationary within each period. Finite cumulants, finite dependence and  are the only assumptions made about the modulations.

The process can be written as  where

and

Thus, the expected value of the signal, is a periodic function. The fixed coefficients  and  determines the shape of. If  or  then  is periodic with period T. If  and  but  or  then  is periodic with period . If the first   and  are zero but not the next then  is periodic with period .

The RMP model is superficially similar to an AM or FM signal but the modulation amplitude can be much larger than the amplitude of the “carrier” (the mean periodicity). The bandwidth of an RMP can be large. It is a type of spread spectrum signal but it is generated by the mechanism underlying the periodic process and is not a communication signal for the applications we have in mind such as active and passive sonar signal processing.

signal coherence spectrum

To provide a measure of the modulation relative to the underlying periodicity Hinich (2000) introduced a concept called the signal coherence spectrum (SIGCOH). This SIGCOH concept is extended in this paper to problem of detecting an RMP in additive stationary noise.

Suppose that the observed signal is  where  and  are defined by expressions (2.2) and (2.3). Assume that the additive noise  is strictly stationary with finite dependence of span D and finite moments. Thus the combined noise and modulation signal  satisfies finite dependence and is stationary within the observation range.

For each Fourier frequency  the value of SIGCOH is

where  is the amplitude of the kth sinusoid,  and

is the discrete Fourier transform (DFT) of .

The amplitude-to-noise standard deviation is  for frequency . Thus it follows that .

Suppose that we know the fundamental period and we observe the signal over M such periods. The mth period is . The estimator of  introduced by Hinich (2000) is

where  is the sample mean of  and  is the sample variance of the residual DFT. This estimator is consistent as.

If  where  then the distribution of  is asymptotically chi-squared with two degrees-of-freedom with a noncentrality parameter  as  (Hinich and Wild, 2001).

These  statistics are asymptotically independently distributed over the frequency band. Thus the distribution of the sum statistic

(3.4)

is approximately chi squared  where  for large values of M.

These chi-squared  statistics and S are used to detect the presence of a hidden periodicity in the signal as shown in the next section.

signal detection

Suppose that we observe a signal . The null hypothesis is  where the noise process  is strictly stationary. The alternative hypothesis is . This alternative is a complicated nonparametric stochastic model. The standard optimal detection theory does not apply to this alternative to the stationary noise hypothesis.

Thus from the asymptotic results stated in the previous section the distribution of  is approximately chi-squared  and S is approximately chi squared  for  when the signal is present and is central  and  respectively for the null hypothesis of noise alone.

The cumulative distribution function of a central chi-squared random variable is . Thus it follows from basic probability theory that under the null hypothesis  has an approximately uniform (0, 1) distribution for each k. We call the display of the U(k) statistics a signal coherence probability spectrum. These probability values are also asymptotically independent as .

This method has been implemented by Hinich in a Fortran 95 program that is available upon request. This simple test augments the standard spectral method. In particular the S test statistic is simple to compute and easy to automate. Furthermore the signal model is realistic when compared to the zero bandwidth harmonics underpinning standard theoretical periodic models. Moreover the assumptions for the modulations are modest. Only stationarity and finite dependence is assumed for the additive noise process. There is no need to assume that the noise is gaussian.

The assumption that the fundamental frequency is known can be relaxed if there is a reasonable belief that there is a RMP in the data within a given band. In activating this procedure, the investigator is essentially makings a sweep of trial fundamental frequencies over the band to find the maximum value of S and its frequency , and then computing the p-value tail probability of the maximum. While this sweep method formally violates the purity of hypothesis testing from a practical perspective, if the p-value of the maximum S is small, say 1.e-5, then any reasonable person would assume that an RMP has been detected with a  fundamental frequency of .

The next section presents simulation results that show that this new method can detect weak RMP signals that are missed by the standard waterfall (spectrogram) approach used in sonar and certain geophysical signal processing applications. The simulations have to use precisely defined modulation processes that have a reasonable number of parameters. Making the simulations very complicated renders the simulations useless for making comparisons between alternative detection methods.

simulation analysis

The model used in the simulations is

where the  are independently distributed random variables with zero means and the additive noise is pure white noise (i.i.d) with variance . Thus the parameters of this model are  and.

In sonar signal processing the hydrophone signals are formed into beams by delay and sum beamforming. The beam signals are blocked into adjacent equal length sections of sampled data. A periodogram is computed for each block and the periodogram values are thresholded to eliminate as many spurious peaks as possible and yet reveal most peaks due to a sinusoid component. These periodograms are stacked into a data structure where the horizontal axis is frequency and the vertical axis is the start time of the block. The display of this data is called a waterfall display or a spectrogram. A periodic signal will show up as a set of harmonically related lines down the waterfall.

Figure 1 presents a waterfall spectrogram plot of 75 consecutive blocks of  frames of length  of artificial data generated by the model in (5.1) with  harmonics,  and  (no additive noise). The units for the signal were chosen so that the fundamental frequency was  Hz and thus the two harmonics are  Hz and  Hz. The periodograms were divided by the maximum value for each block and the plot has a floor off 0.95 and so only values in the interval (0.95, 1.) are shown. The modulation fuzzes the waterfall lines but one can see that there is a periodicity in the signal.

A waterfall plot of the signal coherence probabilities for the same model is shown in Figure 2. This plot also has a floor of 0.95 for the probabilities. The visual signal detection and harmonic analysis is sharper than for the spectrogram plot.

Figure 3 is a spectrogram waterfall plot of the signal with an additive noise standard deviation of  which yields a signal-to-noise ratio (SNR) of -44 dB using the variances of the two frequency bins around each of the three harmonic frequencies. It is apparent from inspection of this figure that the signal is not detectable in this plot.

Figure 4 displays the waterfall plot of the signal coherence probabilities for the -44 dB signal. It is now evident that the signal is detectable in this plot.

In order to estimate the false alarm probability and detection probability of the chi-squared S based test we ran 4000 replications using both a 1% and 5% threshold. For the null hypothesis of only noise the estimated false alarm probabilities were 0.013 and 0.057 respectively. The standard errors of the 1% estimate and 5% estimate are 0.0016 and 0.0034 respectively. Thus the estimates are not statistically different from the target false alarm probabilities.

The estimated probability of detecting the -44 dB signal () at the 1% level is 0.483 for 4000 replications. The estimated probability of detection at the 5% level is 0.709. These results exhibit the power of the RMP test for detecting realistic periodic signals in noise.

References

P. Billingsley,  Probability and Measure, John Wiley, New York, 1979

R.A. Fisher, “Tests of significance in harmonic analysis”, Proceedings of the Royal. Society London, Series A, Vol. 125, 1929, pp. 54-59.

M.J. Hinich, "A Statistical Theory of Signal Coherence," IEEE Journal of Oceanic Engineering, Vol 25, No 2, 2000, pp. 256-261

M.J. Hinich, and P. Wild, "Testing Time-Series Stationarity against an Alternative Whose Mean is Periodic", Macroeconomic Dynamics, Vol 5, 2001, pp. 380-412

M.J. Hinich, "Detecting Randomly Modulated Pulses in Noise,” Signal Processing, Vol 83, 2003, pp.1349-1352

Running Title:

“Detecting Finite Bandwidth Periodic Signals”

Number of pages: 14

Number of Figures: 4

List of Figure Captions:

Figure 1.  RMP Waterfall Plot of Normalized Spectrograms -  &  and 0.95<Peak Values<1.0

Figure 2.  Waterfall Plot of Signal Coherence Probabilities -  &  and 0.95<Peak Values<1.0

Figure 3.  RMP Waterfall Plot of Normalized Spectrograms - f1 = 4 Hz, ,  , SNR = -44dB and 0.95<Peak Values<1.0

Figure 4.  Waterfall Plot of Signal Coherence Probabilities – f1 = 4 Hz, , , SNR = -44dB and 0.95<Peak Values<1.0